## Slide 1: CSE/T/324A Computer Networks Topic 7- Network Layer Internet Protocol
Sarbani Roy
sarbani.roy@jadavpuruniversity.in
Office: CC-5-7
Cell: 9051639328

## Slide 2: Some basics
The term internet is short for “internetworking”
  interconnection of networks with different network access mechanisms, addressing, different routing techniques, etc.
An internet
  Collection of communications networks interconnected by layer 3 switches and/or routers
The Internet - note the uppercase I
  The global collection of individual machines and networks
IP (Internet Protocol)
  most widely used internetworking protocol
  foundation of all internet-based applications

## Slide 3: Internetworking
Internetworking: connecting networks together to make an internetwork or an internet.
  Need for Network Layer
  Internet as a Datagram Network
  Internet as a Connectionless Network

## Slide 4: Protocols of TCP/IP Protocol Suite

## Slide 5: Hop-to-hop Delivery
The physical and data link layer of a network operate locally. These two layers are jointly responsible for data delivery on the network from one node to the next.

## Slide 6: Host-to host delivery
The network layer is responsible for host-to-host delivery and for routing the packets through the routers or switches.

## Slide 7: Network Layer at source and destination

## Slide 8: Network Layer at Router

## Slide 9: Switched Network
In data communications, we need to send messages from one end system to another. If the message is going to pass through a packet-switched network, it needs to be divided into packets of fixed or variable size. The size of the packet is determined by the network and the governing protocol.

## Slide 10: Internet Protocol (IP)
Switching in the Internet is done by using the datagram approach to packet switching at the network layer.
IP provides connectionless (datagram) service
Each packet treated separately
Network layer protocol common to all routers
  which is the Internet Protocol (IP)

## Slide 11: Connectionless Internetworking (General)
Advantages
  Flexible and robust
    e.g. in case of congestion or node failure, packets find their way easier than connection-oriented services
  No unnecessary overhead for connection setup
  Can work with different network types
    does not demand too much services from the actual network
Disadvantage: Unreliable
  Not guaranteed delivery
  Not guaranteed order of delivery
    Packets can take different routes
  Reliability is responsibility of next layer up (e.g. TCP)

## Slide 12: Example Internet Protocol Operation

## Slide 13: Position of IPv4 in TCP/IP protocol suite
The Internet Protocol version 4 (IPv4) is the delivery mechanism used by the TCP/IP protocols.

## Slide 14: IPv4 Datagram format
Packets in the IPv4 layer are called datagrams

## Slide 15
A datagram is a variable-length packet consisting of two parts: header and data. The header is 20 to 60 bytes in length and contains information essential to routing and delivery. It is customary in TCP/IP to show the header in 4-byte sections.

## Slide 16: IP Service Model
Low-level communication model provided by Internet
Datagram
  Each packet self-contained
    All information needed to get to destination
    No advance setup or connection maintenance
  Analogous to letter or telegram
0
4
8
12
16
19
24
28
31
version
HLen
TOS
Length
Identifier
Flag
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data
Header
IPv4 Packet
Format

## Slide 17: IPv4 Header Fields
Version: IP Version
  4 for IPv4
HLen: Header Length
  32-bit words (typically 5)
TOS: Type of Service
  Priority information
Length: Packet Length
  Bytes (including header)
  The total length field defines the total length of the datagram including the header.
Header format can change with versions
  First byte identifies version
Length field limits packets to 65,535 bytes
  In practice, break into much smaller packets for network performance considerations
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 18: Type of Service

## Slide 19: Types of service

## Slide 20: Default types of service

## Slide 21: Codepoints

## Slide 22: IPv4 Header Fields
Identifier, flags, fragment offset  used primarily for fragmentation
Time to live
  Must be decremented at each router
  Packets with TTL=0 are thrown away
  Ensure packets exit the network
Protocol
  Demultiplexing to higher layer protocols
  TCP = 6, ICMP = 1, UDP = 17…
Header checksum
  Ensures some degree of header integrity
  Relatively weak – 16 bit
Options
  E.g. Source routing, record route, etc.
  Performance issues
    Poorly supported
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 23: IPv4 Header Fields
Source Address
  32-bit IP address of sender
Destination Address
  32-bit IP address of destination
Like the addresses on an envelope
Globally unique identification of sender & receiver
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 24: Encapsulation of a small datagram in an Ethernet frame

## Slide 25: Protocol field and encapsulated data

## Slide 26: Fragmentation
A datagram can travel through different networks.
Each router decapsulates the IP datagram from the frame it receives, processes it, and then encapsulates it in another frame.
The format and size of the received frame depend on the protocol used by the physical network through which the frame has just traveled.
The format and size of the sent frame depend on the protocol used by the physical network through which the frame is going to travel.

## Slide 27: Maximum transfer unit (MTU)
Only data in a datagram is fragmented.

## Slide 28: Fields related to fragmentation
Identifier, flags, fragment offset  used primarily for fragmentation
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 29: Flags used in fragmentation

## Slide 30: Fragmentation Offset
This 13-bit field shows the relative position of this fragment with respect to the whole
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 31: Fragmentation and Re-assembly
Different maximum packet sizes for different networks
  routers may need to split the datagrams into smaller fragments
When to re-assemble
  At destination
    Packets get smaller as data travel
      inefficiency due to headers
  Intermediate reassembly
    Need large buffers at routers
    All fragments must go through same router
      Inhibits dynamic routing

## Slide 32: IP Fragmentation
In IP, reassembly is at destination only
Uses fields in header
  Data Unit Identifier – In order to uniquely identify datagram – all fragments that belong to a datagram share the same identifier
    Source and destination addresses
    Upper protocol layer (e.g. TCP)
    Identification supplied by that layer
  Data length
    Length of user data in octets (if fragment, length of fragment data)
    Actually header contains total length incl. header but data length can be calculated
  Offset
    Position of fragment of user data in original datagram (position of the first byte of the fragment)
    In multiples of 64 bits (8 octets)
  More flag
    Indicates that this is not the last fragment (if this flag is 1)

## Slide 33: Fragmentation Example

## Slide 34
Fragmentation example

## Slide 35
Detailed fragmentation example

## Slide 36: IP Fragmentation Example #1

## Slide 37: IP Fragmentation Example #2

## Slide 38: IP Fragmentation Example #3

## Slide 39: IP Reassembly

## Slide 40
A packet has arrived with an M bit value of 0. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?
Solution
If the M bit is 0, it means that there are no more fragments; the fragment is the last one. However, we cannot say if the original packet was fragmented or not. A nonfragmented packet is considered the last fragment.
Example

## Slide 41
A packet has arrived with an M bit value of 1. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?
Solution
If the M bit is 1, it means that there is at least one more fragment. This fragment can be the first one or a middle one, but not the last one. We don’t know if it is the first one or a middle one; we need more information (the value of the fragmentation offset). See also the next example.
Example

## Slide 42
A packet has arrived with an M bit value of 1 and a fragmentation offset value of zero. Is this the first fragment, the last fragment, or a middle fragment?
Solution
Because the M bit is 1, it is either the first fragment or a middle one. Because the offset value is 0, it is the first fragment.
Example

## Slide 43
A packet has arrived in which the offset value is 100. What is the number of the first byte? Do we know the number of the last byte?
Solution
To find the number of the first byte, we multiply the offset value by 8. This means that the first byte number is 800. We cannot determine the number of the last byte unless we know the length of the data.
Example

## Slide 44
A packet has arrived in which the offset value is 100, the value of HLEN is 5 and the value of the total length field is 100. What is the number of the first byte and the last byte?
Solution
The first byte number is 100 × 8 = 800. The total length is 100 bytes and the header length is 20 bytes (5 × 4), which means that there are 80 bytes in this datagram. If the first byte number is 800, the last byte number must be 879.
Example

## Slide 45: Checksum
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 46: Checksum
The error detection method used by most TCP/IP protocols is called the checksum.
The checksum protects against the corruption that may occur during the transmission of a packet. It is redundant information added to the packet.
The checksum is calculated at the sender and the value obtained is sent with the packet.
The receiver repeats the same calculation on the whole packet including the checksum.
If the result is satisfactory, the packet is accepted; otherwise, it is rejected.

## Slide 47: Checksum in one’s complement arithmetic

## Slide 48: Checksum
Checksum in IP covers only the header, not the data.
The header is divided into 16-bit sections. All the sections are added and the sum is complemented. The result is inserted in the checksum field.

## Slide 49: Options
The header of the IP datagram is made of two parts: a fixed part and a variable part. The fixed part is 20 bytes long and was discussed in the previous section. The variable part comprises the options, which can be a maximum of 40 bytes.
Options, as the name implies, are not required for a datagram. They can be used for network testing and debugging. Although options are not a required part of the IP header, option processing is required of the IP software.

## Slide 50: Option format

## Slide 51: Categories of options

## Slide 52: No operation option

## Slide 53: End-of-option option

## Slide 54: Record-route option

## Slide 55: Record-route concept

## Slide 56: Strict-source-route option

## Slide 57: Strict-source-route option

## Slide 58: Loose-source-route option

## Slide 59: Time-stamp option

## Slide 60: Use of flags in timestamp

## Slide 61: Timestamp concept

## Slide 62: ping and traceroute
One of the utilities available in UNIX to check the traveling of the IP packets is ping.
We can also use the ping utility with the -R option to implement the record route option.
The traceroute utility can also be used to keep track of the route of a packet.
The traceroute program can be used to implement loose source routing. The -g option allows us to define the routers to be visited, from the source to destination.

## Slide 63: IPv4 to IPv6
The network layer protocol in the TCP/IP protocol suite is currently IPv4.
Although IPv4 is well designed, data communication has evolved since the inception of IPv4 in the 1970s.
IPv4 has some deficiencies that make it unsuitable for the fast-growing Internet.

## Slide 64
IPv6 datagram header and payload

## Slide 65
Format of an IPv6 datagram

## Slide 66
Next header codes for IPv6

## Slide 67
Priorities for congestion-controlled traffic

## Slide 68
Priorities for noncongestion-controlled traffic

## Slide 69
Comparison between IPv4 and IPv6 packet headers

## Slide 70
Extension header types

## Slide 71
Comparison between IPv4 options and IPv6 extension headers

## Slide 72: Transition from IPv4 to IPv6
Because of the huge number of systems on the Internet, the transition from IPv4 to IPv6 cannot happen suddenly.
It takes a considerable amount of time before every system in the Internet can move from IPv4 to IPv6.
The transition must be smooth to prevent any problems between IPv4 and IPv6 systems.

## Slide 73
Three transition strategies

## Slide 74
Dual stack

## Slide 75
Tunneling strategy

## Slide 76
Header translation strategy

## Slide 77
Header translation